## Slide 1
MassChroBook
Guide for users
National Institute of Genetics
Kazusa DNA Research Institute
Sakura Scientific Co. Ltd.

## Slide 2
MassChroBook is a collection of 2-dimensional (2D) mass chromatogram images which are obtained from metabolome analysis of various samples using liquid chromatography (LC) - mass spectrometry (MS). A visualization of the peak detection profiles will help an intuitive understanding of the chemical differences between the samples.
About MassChroBook
http://metabolites.in/foods
Food Metabolome Repository
MassChroBook and the detailed analysis data are available at the “Metabolome Repository" websites below.
Plant Metabolome Repository
http://metabolites.in/plants
Thing Metabolome Repository
http://metabolites.in/things
The data in TMR are not comparable to those in FMR and PMR because different analytical instruments and conditions were used.

## Slide 3
1) Title
3) Sample photo
2) 2D-mass chromatogram
Page Structure

## Slide 4
The data of measurement of compound masses by mass spectrometry (MS) after separation by liquid chromatography (LC).
x-axis: Retention time (min)
A: Amino acids, etc.
B: Various secondary metabolites, etc.
C: Lipids, etc.
E: Peptides, etc.
1) 2D-Mass Chromatogram 1/2
x-axis: The retention time of LC (min). Hydrophilic and hydrophobic compounds are eluted in the earlier and later, respectively.
y-axis: The mass to charge ratio (m/z) measured by MS.
Red spots: Compounds detected. The color strength shows the detection intensity.
y- axis: Mass to charge ratio (m/z)
General positions:
A
B
C
D

## Slide 5
The peak signals detected after 32.5 min are poorly reproducible because compounds strongly retained to the column are eluted around here.
Signals not derived from the samples
The internal standard (IS, 7-hydroxy-5-methylflavone) is detected at around 21.4-21.6 min.
Signals detected in 0-3 min and 38.5-40.5 min are from the calibrants for calibration of m/z values. During this time, the eluent from the LC column was discarded.
Keep in mind that a number of peaks are detected in the mock data (negative control).
Other characteristics:
1) 2D-Mass Chromatogram 2/2
IS
discarded
Calibrants
poory
reproducible
discarded

## Slide 6
The sample photo is an image of the sample and it is not necessarily from the very sample which was used for the analysis.
Not only the pictures taken in our lab but also the pictures obtained from free picture resources are used. We greatly appreciate the following websites for their provision of beautiful photos.
Photo AC photo-ac.com
Forest in Full Bloom forest17.com
Food foto food.foto.ne.jp
Photock photock.jp
Ashinari' web site ashinari.com
Sozai page sozai-page.com
2) Sample Photo

## Slide 7
A typical mock sample (positive mode)

## Slide 8
A typical mock sample (negative mode)